## Slide 1
Motorized Robotic Hand Controlled by Surface Electromyography (sEMG)
Jay E. Bernstein, David J. Mora, Juan R. Ortiz
Advised by Dr. Norali Pernalete
6mm 8mm 10mm 20mm 30mm. 32Point = 0.5 inch High
Picture of Complete Project Here
Abstract
The objective of this project was to discover the fundamentals of signal acquisition and processing, in a situation requiring extremely precise hardware requirements in order to achieve both common mode signal rejection and extremely high gain. Because this is a medical device, considerations of safety had to be made as well. The final product is a printed circuit board designed around the Texas Instruments INA82x that handles differential gain, with input resistance to limit the shock hazard were a fault to occur. The amplified input signal is processed so that a microcontroller is able to determine what command the signal is closest to.
Chart: Recorded Vs Processed Signal From Probe
Block Diagram
Surface EMG Pads
Amplifier
Microcontroller (Teensy 4.1)
Robotic Hand
Normalize, Rectify, and Amplify ADC Input
Finger Detection Algorithm
Capture 1000 Samples at 40kHz with ADC
Protected Inputs to Instrumentation Amplifier IC
AC Coupled and Buffered Output
Software/Hardware Overview
Picture of Probes on Arm, or many smaller pictures of physical setup
Conclusion
Compare amplifier characteristics between discrete inamp, breadboarded ina129, and assembled hardware. Design tradeoffs made, such as removing 60hz HP filter. Nature of MUAPs, long spacing and frequency components. Power supply noise rejection and grounding issues with amplifier. Conclude with what went right what went wrong, what to improve next time
References and Inspiration
https://people.ece.cornell.edu/land/courses/ece4760/FinalProjects/f2016/mh2298_jyh37_sv376/mh2298_jyh37_sv376/mh2298_jyh37_sv376/index.html
Chart: Gain Comparison of Probe Board Revisions
| 110 | 150 | 230 | 340 | 690 | 990 | 1410 | 2020 | 2900 | 4160 | 5990 | 8620 | 12400 | 17780
Revision 1 Hardware | -7.5 | -7.7 | -7.6 | -7.8 | -7.9 | -8.4 | -8.8 | -9.6 | -11.1 | -13 | -15.4 | -18.4 | -21.2 | -24.4
Revision 2 Hardware | -7.1 | -7.1 | -7 | -7.1 | -7.2 | -6.9 | -6.7 | -6.9 | -7.7 | -8.3 | -9.2 | -9.7 | -10.1